K32 PANEL CUBICLES

To be read with preliminaries and general conditions

Manufacturer: Toilet cubicles Ireland, Unit 15 Donore Business pk, Donore rd, Drogheda, Co Louth. Email: info@toiletcubiclesireland.ie Web: www.toiletcubiclesireland.ie

Product reference: edge20 full height toilet cubicles

Doors: 20mm solid grade laminate (SGL) same colour both sides

Pilasters: 20mm solid grade laminate (SGL) same colour both sides

Core material: Not required self supported board black core

Finish: Subject to SGL manufacturer selected

Colour: SGL selection or specified colours subject to size

Edge treatment: Square edge with pilaster and door reverse rebated to form inline flush faced lines all other edges smooth profile finish

Panels: 20mm solid grade laminate (SGL)

Core material: Not required self supported board black core

Finish: Subject to SGL manufacturer selected

Colour:Toilet Cubicles Ireland SGL selection or specified colours subject to size

Edge treatment: Square edge and smooth profile finish

Head Rail: Rigid polished aluminium section with bull-nosed leading edge

Finish: Polished

Legs: Not required (can be raised of floor level if desired with legs)

Ironmongery & Accessories: Stainless steel Indicator bolt, hinges & buffered coat hook, wall channel brackets and pilaster fixings

Finish/Colour: stainless steel

Dimensions: Unless stipulated here dimensions are as the technical data provided for edge20

Other requirements: Complete with outward opening doors to ambulant and enlarged cubicles as requested. Cubicles with inward opening doors can be set out to maintain 450mm diameter manoeuvring space within the cubicle. Pilasters and partitions floor fixed or set in channel brackets. Partition can be raised on a leg if required.