K32 PANEL CUBICLES

To be read with preliminaries and general conditions

Manufacturer:  Toilet Cubicles Ireland, Unit 15 Donore Business pk, Donore rd, Drogheda, Co Louth. Ph/Fax 041-9818148

Email: info@toiletcuiclesireland.ie Web: www.toiletcubiclesireland.ie

Product reference: edge44 toilet cubicles

Doors: 44mm door blank surfaced in selected veneer (Option of high pressure laminate available)

Pilasters: 44mm door blank surfaced in selected veneer (Option of high pressure laminate available)

Core material: Standard door blank construction

Finish: Two coat A/C lacquer

Colour: Standard range of wood veneers or hpl laminate

Edge treatment: 10mm/20mm hardwood edge with veneer over faced pilaster and door reverse rebated to form inline flush faced lines

Panels: 30mm core surfaced in selected veneer (Option of high pressure laminate available)

Core material: Moisture resistant chipboard

Finish: Two coat A/C lacquer

Edge treatment: 10mm/20mm hardwood edge with veneer over faced

Head Rail: Not required (Over panel can be provided if required)

Finish: Two coat A/C lacquer

Colour: Toilet Cubicles Ireland veneer selection

Legs: Not required

Ironmongery & Accessories: Stainless steel Indicator bolt, hinges & buffered coat hook

Finish/Colour: stainless steel

Dimensions: Unless stipulated here dimensions are as the technical data provided for edge44

Other requirements: Complete with outward opening doors to ambulant and enlarged cubicles as requested. Cubicles with inward opening doors can be set out to maintain 450mm diameter manoeuvring space within the cubicle. Pilasters and partitions mounted on hard wood blocks, pilasters and door junction invisible fixed no face fixings.