K32 PANEL CUBICLES

To be read with preliminaries and general conditions

Supplier : Toilet Cubicles Ireland, Unit 15 Donore Business Pk, Donore Rd, Drogheda Co louth ph/fax: 0035341-9818148

Email: info@toiletcubiclesireland.ie Web: www.toiletcubiclesireland.ie

Product reference: ethos toilet cubicles

Pilasters: Slim-line profiles formed stainless steel, vertical edges tight radius finished

Head Rail: Stainless steel head-rail fixed above pilaster profiles

Finish: Satin polished

Doors: 18mm moisture resistant chipboard faced both sides with high pressure laminate (HPL)

Core material: Moisture resistant chipboard (to V313)

Finish: Subject to HPL manufacturer selected

Colour: Toilet Cubicles Ireland HPL selection or specified colours subject to size

Edge treatment: Square lipped to match or contrast face surface in 1mm PVC or HPL

Panels: 18mm moisture resistant chipboard faced both sides with high pressure laminate (HPL)

Core material: Moisture resistant chipboard (to V313)

Finish: Subject to HPL manufacturer selected

Colour:Toilet Cubicles Ireland HPL selection or specified colours subject to size

Edge treatment: Square lipped to match or contrast face surface in 1mm PVC or HPL

Legs: Adjustable cylindrical stainless steel pedestal leg located on the partition 200mm back from face of adjoining pilaster providing floating cubicle appearance

Ironmongery & Accessories: Sprung loaded pivot hinges & dampener/Buffered coat hook/ DDA compliant lever operated indicator bolt, circular face plate and easy emergency release facility, bracket fixings to wall and pilaster

Finish: Stainless steel/stainless steel matched effect

Dimensions: Unless stipulated here dimensions are as the technical data provided for ethos

Other requirements: Complete with outward opening doors to ambulant and enlarged cubicles where requested. Cubicles with inward opening doors can be set out to maintain 450mm diameter manoeuvring space within the cubicle. Optional door material veneer or glass at surcharge