K32 PANEL CUBICLES

To be read with preliminaries and general conditions

Supplier : Toilet Cubicles Ireland, Unit 15 Donore business Pk, donore Rd, Drogheda co Louth Ph/ Fax 041-9818148 Email: info@toiletcubiclesireland.ie Web: www.toiletcubiclesireland.ie

Product reference: ethos + toilet cubicles

Pilasters: Slim-line profiles formed stainless steel, vertical edges radius finished

Head Rail: Stainless steel head-rail fixed above pilaster profiles

Finish: Satin polished

Doors: 12/13mm solid grade laminate (SGL) same colour both sides

Core material: Not required self supported board black core (SGL)

Finish: Subject to SGL manufacturer selected

Colour: Toilet cubicles Ireland SGL selection or specified colours subject to size

Edge treatment: Machined smooth profile or square (Black core always visible)

Panels: 12/13mm solid grade laminate (SGL) same colour both sides

Core material: Not required self supported board black core (SGL)

Finish: Subject to SGL manufacturer selected

Colour: Toilet Cubicles Ireland SGL selection or specified colours subject to size

Edge treatment: Machined smooth profile or square (Black core always visible)

Legs: Adjustable cylindrical stainless steel pedestal leg located on the partition 200mm back from face of adjoining pilaster providing floating cubicle appearance

Ironmongery & Accessories: Sprung loaded pivot hinges & dampener/Buffered coat hook/ DDA compliant lever operated indicator bolt with circular face plate easy emergency release facility, bracket fixings to wall and pilaster

Finish: Stainless steel/stainless steel matched effect

Dimensions: Unless stipulated here dimensions are as the technical data provided for ethos+

Other requirements: Complete with outward opening doors to ambulant and enlarged cubicles where requested. Cubicles with inward opening doors can be set out to maintain 450mm diameter manoeuvring space within the cubicle.