K32 PANEL CUBICLES

To be read with preliminaries and general conditions

Supplier: Toilet cubicles Ireland, Unit 15, donore business pk,donore rd, Drogheda

Co louth. Email: info@toiletcububiclesireland.ie Web: www.toiletcubiclesireland.ie

Product reference: ethos v toilet cubicles

Pilasters: Slim-line profiles formed stainless steel, vertical edges radius finished

Head Rail: Stainless steel head-rail fixed above pilaster profiles

Finish: Satin polished

Doors: 18mm moisture resistant chipboard faced both sides with Veneer

Core material: Moisture resistant chipboard (to V313)

Finish: Two coat A/C lacquer

Colour: Toilet cubicles Ireland V selection

Edge treatment: 10mm hardwood edge bonded to core board and over faced with veneer

Panels: 18mm moisture resistant chipboard faced both sides with Veneer

Core material: Moisture resistant chipboard (to V313)

Finish: Two coat A/C lacquer

Colour: Toilet cubicles Ireland V selection

Edge treatment: 10mm hardwood edge bonded to core board and over faced with veneer

Legs: Adjustable cylindrical stainless steel pedestal leg located on the partition 200mm back from face of adjoining pilaster providing floating cubicle appearance

Ironmongery & Accessories: Sprung loaded pivot hinges & dampener/Buffered coat hook/ DDA compliant lever operated indicator bolt with circular face plate and easy emergency release facility, bracket fixings to wall and pilaster

Finish: Stainless steel/stainless steel matched effect

Dimensions: Unless stipulated here dimensions are as the technical data provided for ethos v

Other requirements: Complete with outward opening doors to ambulant and enlarged cubicles where requested. Cubicles with inward opening doors can be set out to maintain 450mm diameter manoeuvring space within the cubicle.