K32 PANEL CUBICLES

To be read with preliminaries and general conditions

Manufacturer: Toilet Cubicles Ireland,Unit 15 donore business pk, Donore rd Drogheda, Co Louth ph/Fax 041-9818148 Email: info@toiletcubiclesireland.ie Web: www.toiletcubiclesireland.ie

Product reference: function toilet cubicles

Doors: 18mm moisture resistant chipboard faced both sides with high pressure laminate (HPL)

Core material: Moisture resistant chipboard (to V313)

Finish: Subject to HPL manufacturer selected

Colour: Toilet Cubicles Ireland HPL selection or specified colours subject to size

Edge treatment: All edges lipped with matching/contrasting durable PVC

Panels: 18mm moisture resistant chipboard faced both sides with high pressure laminate (HPL)

Pilasters: 18mm/30mm moisture resistant chipboard faced both sides with (HPL)

Core material: Moisture resistant chipboard (to V313)

Finish: Subject to HPL manufacturer selected

Colour: Toilet Cubicles Ireland HPL selection or specified colours subject to size

Edge treatment: Pilaster vertical edges post-formed all other edges are square lipped with matching/contrasting durable PVC

Head Rail: Rigid polished aluminium section with bull-nosed leading edge

Finish: Polished

Legs: Polished aluminium rectangular design, partition fixed, adjustable to varying floor levels

Ironmongery & Accessories: Aluminium pivot hinges/Coat hook/DDA compliant slide operated indicator bolt with elliptical face plate/Emergency release facility. Channel bracket partition fixings.

Finish/ Colour: Polished Aluminium

Dimensions: Unless stipulated here dimensions are as the technical data provided for function+pf

Other requirements: Complete with outward opening doors to ambulant and enlarged cubicles as requested. Cubicles with inward opening doors can be set out to maintain 450mm diameter manoeuvring space within the cubicle, this may require an extended pilaster detail