function technical data

Overall Dimensions

Overall cubicle height: 1980mm (can be provided up to 3000mm high)

Overall cubicle width: 750mm-900mm (can be provided wider with additional pilaster panels)

Overall ground clearance: 160mm (can be provided lower subject to partition construction)

Component Dimensions

Partition height: 1820mm (can be provided up to 3000mm high)

Partition depth: 1520mm (can be provided up to 2100mm subject to partition construction)

Partition thickness: 20mm

Pilaster height: 1820mm (can be provided up to 3000mm high)

Pilaster width: 80mm minimum up to 200mm

Pilaster thickness: 30mm

Door height: 1780mm (can be provided up to 2995mm)

Door width: 600mm-750mm (can be provided wider subject to partition depth/pilaster panel)

Door thickness: 20mm