Specifications (wood Locker).

09

Wooden Lockers

MFC locker bodies, available in a variety of height combinations and widths.

• MFC bases, tops and shelves.

• Doors and matching end panels from solid hardwoods veneered or HPL (High Pressure Laminate) faced MDF board.

• Various plinth options.

Features:

• Melamine faced chipboard bodies with dowel and screw construction, available in a choice of colours and timber effect finish.

• Base, top and shelf units from the same material with 2mm PVC edge banding to front edges.

• Full width hanging rails are provided in all compartments of 900mm or more high, captive coat hangers are available as an option. Shoe shelves can also be provided.

Doors:

• 19mm solid hardwoods.

• 19mm MDF faced with true wood veneers.

• 19mm MDF faced with 0.9mm high-pressure laminate.

• Matching end and infill panels are provided according to site requirements.

Fixtures & Fittings:

Fixtures and Fittings to complete the fit out.

• Well lockers with canterleaver bench seats

• Golf storage lockers

• Valuables and holdall lockers

• Vanity units and shelves

• Changing cubicles

• Garment hanging rails

• Cupboards and TV monitor or cabinets

• Towel drops and storage bins

• Mirrors and notice boards

• Lighting pelmets

• Capping rails

• Plinths

• Bench seating and stools

Standard Wood Finish:

• Oak

• Ash

• Steamed Beach

• Sapelle

locker configurations

Wooden Locker with wood Doors For Dry Areas

Size & Configuration

• Height - 900mm / 1500mm / 1700mm / 1800mm / 2000mm / 2200mm.

• Width - 300mm / 400mm / 500mm.

• Double Duplex - 650mm.

• Depth - normally 520mm or 600mm

Tierage:

• 1 tier, single compartments with additional shelf at 300mm down from top.

• 2 tier, 2 equal height compartments with coat hooks.

• 2 tier, 2 equal compartments with integral seats“well locke r ”.

• 3 tier, 3 equal compartments.

• 3 tier, unequal, 1 half-height compartments with coat hooks over 2-quarter height.

• 4 tier, 4 equal compartments.

• 2 tier, Z-lockers, 2 equal height compartments with coat hooks.

Support Plinths:

• Pre-cast concrete plinth (by others).

• Timber framed 100mm or 150mm high.

• 390mm wide compact grade laminate/hardwood timber seat slat.

• Angle fix to wall.