N10 GENERAL FIXTURES VANITY UNITS ( compact laminate).

To be read with preliminaries and general conditions

Supplier: Toilet cubicles Ireland, Unit 15 donore business pk, Donore rd, Drogheda, Co Louth. Ph/fax 041-9818148

Email: info@toiletcubiclesireland.ie Web: www.toiletcubiclesireland.ie

Product reference: V2 vanity unit

Vanity top: 12mm/13mm solid grade laminate (SGL) for maximum protection against water

Up stand: 100mm loose SGL profile finished square edge

Apron: 200mm loose SGL profile down stand finished square edge

Core material: Not required self supported board black core

Finish: Subject to SGL manufacturer selected

Colour:  SGL selection card

Edge treatment: Machined smooth profile or square (Black core always visible)

Panels: 12mm/13mm solid grade laminate (SGL) for maximum protection against water

Core material: Not required self supported board black core

Finish: Subject to SGL manufacturer selected

Colour: Subject to SGL manufacturer selected

Edge treatment: Machined smooth profile or square (Black core always visible)

Accessories: Concealed Keku ‘lift off’ brackets.

Support system: Treated softwood framework, notched and screwed made to measure and site assembled.

Dimensions: Unless stipulated dimensions as the technical data provided for V2 vanity units

Other requirements: Cut outs for basins marked on site by builder