N10 GENERAL FIXTURES VANITY UNITS (Natural Stone).

To be read with preliminaries and general conditions

Supplier: Toilet Cubicles Ireland, Unit 15 Donore Business pk, Donore rd, Drogheda, Co Louth. Email: info@toiletcubiclesireland.ie Web: www.toiletcubiclesireland.ie

Product reference: V4

Vanity top: 30mm natural stone material polished, factory cut outs

Up stand: 100mm  profile finished

Apron: 200mm  down stand

Core material: Not required self supported fixed to ladder frames

Finish: Subject to client preference

Colour:  Toilet cubicles Ireland range of  granite, marbles and limestone’s.

Edge treatment: Machined smooth polished profile or square

Panels: MFC/HPL/SGL/VENEER

Core material: subject to face

Finish: Subject to face manufacturer selected

Colour: stone selection

Edge treatment: polished

Accessories: Concealed Keku ‘lift off’ brackets.

Support system: Treated softwood framework, notched and screwed made to measure and site assembled.

Dimensions: Unless stipulated dimensions as the technical data provided for V4 vanity units

Other requirements: Cut outs in factory, basin & tap template required.